## Slide 1: Net Zero CO2 Emissions plan of Japan by 2050
Submitted To: Presented By:
Dr. Anna Agarwal Saransh Sharma
Dr. Rajeev Jindal
1

## Slide 2: Energy Demand in 2020
Energy Consumption by each sector
Energy consumption from different sources by each sector
Overall oil accounted for 50.4 % of total energy consumption dominating Transport, agriculture and fishing sector. Electricity accounted for more than half of consumption for Residential, Commercial and public services sector and for 30% overall.
Source-Energy Statistics Data Browser – Data Tools - IEA
2

## Slide 3: Energy Supply in 2020
Coal and oil accounts for 6.20 EJ and 4.27 EJ
More than 88 % dependency on fossil fuels
Less than 9 % from renewable (Hydro, wind and solar, biofuels and waste)
Total primary energy supply by different sources
4.27 EJ
6.20 EJ
6.20 EJ
0.644 EJ
Source-Energy Statistics Data Browser – Data Tools - IEA
3

## Slide 4: CO2 Emissions
Chart: Years
The total emission reduction in 2050 in comparison to what current trends leads to
BAU - 57.78 %
APS - 70 %
LCET- 100 %
2020 CO2 emissions – 284 Mt-C
2023 CO2 emissions - 334 Mt-C
Mainly from fossil fuel energy supply (16.67 EJ).
Source - Energy Outlook and Energy-Saving Potential in East Asia 2023 (eria.org) ; CO2 emissions - Our World in Data
4

## Slide 5: Demand side
Transition of Primary energy consumption in LCET case scenario
Assumptions-
The cost, insurance, and freight (CIF) prices for crude oil, coal, and liquified natural gas (LNG) will increase from 2010 to 2050 by 67%, 27%, and 34%, respectively.
The CIF prices for hydrogen will be 330 JPY/kg-H2 (3.0 USD/kgH2 in 2050.
The population will decline to 97 million by 2050
The house-hold population will be 47.2 million.
Source - Japan's pathways to achieve carbon neutrality by 2050 – Scenario analysis using an energy modeling methodology – ScienceDirect
5

## Slide 6: Demand side
Decarbonisation of electricity which accounted for 3.8 EJ energy consumption in 2050.
Fuel shifting from gasoline to electricity.
The share of electricity and hydrogen increases from 27% (3.8 EJ) in 2010 to 59% (5.7 EJ) in 2050.
Hydrogen will play major role as the country has less CCS facilities and biomass resources availability in dispatchable powerplants (2 EJ in 2050).
6

## Slide 7: Supply side
Assumptions-
Maximum Nuclear power generation capacity by 2050 will be 19 GW.
(generation capacity of 47.5 GW in 2011)
Maximum Renewable power generation capacity of 337.6 GW by 2050.
Transition of Primary energy supply in base case scenario
Source - Japan's pathways to achieve carbon neutrality by 2050 – Scenario analysis using an energy modeling methodology - ScienceDirect
7

## Slide 8: Supply side
Systems comprising low carbon energy sources such nuclear and hydrogen contribute to 3.4 EJ (60%)
650 TWh energy generation from renewables
Solar and wind will become 4.5 and 11.2 times the current capacities.
178.4 Mt-C of CO2 emissions reduction by reducing share of fossil fuel by 10.47 EJ (62%)
8

## Slide 9: Carbon Capture
Assumptions-
Maximum CO2 storage of 81.88 Mt-C/yr
Direct air capture carbon storage and Bio energy with cabon capture and storage available by 2030
Post-combustion CO2 capture technologies using monoethanolamine
Source - Japan's pathways to achieve carbon neutrality by 2050 – Scenario analysis using an energy modeling methodology - ScienceDirect
9

## Slide 10: Net Zero Transition
58.68 Mt-C of CO2 will be removed by 2050 through DACCS and BECCS processes (Carbon Capture)
178.4 Mt-C of CO2 emissions reduction by reducing share of fossil fuel by 10.47 EJ and using low carbon energy sources (Supply side)
Remaining 35.85 Mt-C reduction will be due to energy efficiency and population decline
10

## Slide 11: Additional Policy measure
The 3 E’s principle(environment, energy security, economic efficiency + safety) is the key to Japan policy. More focus on energy security and economic efficiency should be implied.
Policies that promote development of dispatchable capacity and adjust the capability for output fluctuation of renewables.
Policies related to hydrogen imports for stable supply in place of fossils.
11